LINUX 5-MINUTE PLAN
  - Step 1: Change every user's password:
    - HISTFILE=/dev/null awk -F: '{print $1":CryptoDATA001$$"}' /etc/passwd | sudo chpasswd
  - Step 2: Reset PAM configuration:
    - sudo pam-auth-update --force
  - Step 3: Fix SSH authentication:
    - /etc/ssh/sshd_config: “UsePAM yes” -> “UsePAM no” (Line 80ish)
    - sudo systemctl restart sshd
    - cat /etc/apt/sources.list OR ls /etc/apt/sources.list.d/
      - Check for naughty repos real quick and remove any standouts
  - Step 4: Configure iptables:
iptables -F	Flush all chains
iptables -X	Delete all chains
iptables -Z	Reset packet & byte counter in chains
iptables -L -nv --line-numbers	Show ruleset

    - PACKAGE INSTALL FOR PERSISTENT RULES ON REBOOT (DO FIRST):
      - sudo apt install iptables-persistent
      - sudo dnf install iptables-services (RED HAT ONLY)
CUSTOM RULESET (FOLLOW IN ORDER) / only need ‘sudo’ if not root
sudo iptables -A INPUT -j ACCEPT	Create allow any-any rules while creating custom ruleset (prevents loss in scoring)
sudo iptables -A OUTPUT -j ACCEPT
sudo iptables -P INPUT DROP	Change the default chain rules to drop all packets if none of the rules match
sudo iptables -P FORWARD DROP
sudo iptables -P OUTPUT DROP

sudo iptables -A INPUT -i lo -j ACCEPT	Allow traffic to and from the loopback interface
sudo iptables -A OUTPUT -o lo -j ACCEPT
sudo iptables -A INPUT -m conntrack --ctstate ESTABLISHED,RELATED -j ACCEPT	Uphold current connections with the system (will also prevent a lockout from ssh when removing the first rule)
sudo iptables -A OUTPUT -m conntrack --ctstate ESTABLIHSED,RELATED -j ACCEPT
sudo iptables -A INPUT -p tcp --dport 22 -s <VPN subnet> -m conntrack --ctstate NEW -j ACCEPT	Allows all ssh connections in and out of the system; can add IPs in here (syntax in docs)
sudo iptables -A OUTPUT -p tcp -m multiport --dports 80,443 -m conntrack --ctstate NEW -j ACCEPT	Allow HTTP/HTTPS connections to be created outbound
sudo iptables -A OUTPUT -p udp --dport 53 -s 1.1.1.1 -j ACCEPT	Allow outbound DNS requests only to public DNS server (or the Windows AD DNS, but it might be poisoned)
sudo iptables -A OUTPUT -p tcp --dport 53 -s 1.1.1.1 -j ACCEPT

sudo iptables -A INPUT -s <scoring-ip> -m conntrack --ctstate NEW -j ACCEPT	Allow the scoring engine to reach the box directly both inbound and outbound
sudo iptables -A OUTPUT -d <scoring-ip> -m conntrack --ctstate NEW -j ACCEPT
*Consult iptables documentation for port specific rules*	Get creative—add rules for certain protocols/other IPs (ping, specific services, ftp, ntp server traffic, etc.)

sudo iptables -A INPUT -m limit --limit 20/hr -j LOG --log-prefix “[netfilter] INPUT:DROP: ” --log-level 7	Any packet that is going to be dropped will be added to the syslog with the specified prefix
sudo iptables -A OUTPUT -m limit --limit 20/hr -j LOG --log-prefix “[netfilter] OUTPUT:DROP: ” --log-level 7

sudo iptables -D INPUT 1	Remove allow any-any rules when ruleset is *mostly* complete
sudo iptables -D OUTPUT 1

    - SAVE RULES WHEN DONE!!!
      - sudo sh -c “iptables-save > /etc/iptables/rules.v4”
    - Check other tables real quick
      - sudo iptables -L -nv <mangle, nat, raw, security>
    - View the logs if necessary
      - journalctl -k | grep ‘\[netfilter\]’

    - EXTRA INFO FOR RED HAT (Fedora/Rocky/CentOS)
      - sudo systemctl stop firewalld
      - sudo systemctl disable firewalld
      - sudo systemctl start iptables
      - sudo systemctl enable iptables

  - Step 5: Backup EVERYTHING:

    - INITIALIZATION
      - sudo apt install git
      - cd /
      - git init .
      - git add /etc/ssh/sshd_config
      - git add /usr/bin/ls
      - git add /usr/bin/cat
      - git add /usr/bin/ssh
      - git add /usr/lib/ssh
      - git add /etc/ssh
      - git add /usr/bin/echo
      - git add /path/to/important/file (do this for every file you want tracked)
      - git commit (saves changes to a specific “commit”)

    - MONITORING AND MAINTENECE
      - git diff (shows difference between last commit and current state of files)
      - git log (lists commits)
      - git checkout <commit_id> --force (reverts to a specific commit)
      - git revert (reverts to last commit)
      - git status (see what commit you’re on)

POST 5-MINUTES
  - Step 1: Update packages:
    - CHECK REPOS IN DEBIAN (Debian/Ubuntu/openSUSE)
      - cat /etc/apt/sources.list
      - ls /etc/apt/sources.list.d/
    - CHECK REPOS IN RED HAT (Fedora/Rocky/CentOS)
      - ls /etc/yum.repos.d
      - cat /etc/yum.repos.d/*.repo
    - UPDATE THE SYSTEM PACKAGES
      - sudo apt clean
      - sudo apt update && sudo apt upgrade
      - sudo dnf update && sudo dnf upgrade
        - Establish a second terminal connection while running this

  - Step 2: Lock out bad accounts kill current sessions:
    - cat /etc/passwd
    - cat /etc/group
      - Check all users and/or groups currently on the system
      - Can ‘chattr -i /etc/groups’ to lock the config
    - sudo usermod -L && sudo usermod -s /usr/sbin/nologin <user>
      - Disable the specified account and remove its shell access
    - sudo truncate -s 0 ~/.ssh/authorized_keys
      - Command to remove naughty keys... (if not already done)
    - who -u and lastlogin and netstat -atn | grep ':22'
      - Check logins from users and use pkill/kill to terminate them
      - pkill -9 -t {term-name} or kill -9 {PID}

  - Step 3: Check repeated processes (systemd timers and crontab):
    - sudo systemctl list-timers --all
      - Insight into red team implants
      - crontab -e
      - Check to make sure there aren’t any naughty jobs
      - Add the following lines (first checks if designated service is down and restarts it; second copies files to backup path)
    - * * * * * systemctl is-active --quiet <service_name> || systemctl restart <service_name>
    - * * * * * cp /etc/ssh/sshd_config <file_path>
  - Step 4: Look for signs of Red Team & manual threat hunting:
    - Search major binaries/anywhere on the system for Red Team implants
    - Typically, they are larger files (MBs in size) with names slightly different from services, etc.
      - sudo find / -type f -executable -size +1M
        - Find executable files throughout the system >1MB
    - Utilize process listing/memory forensics to our advantage
      - ps -eLf
      - ps faux
      - dpkg -V
        - CHECKS INSTALLED PACKAGES FOR CHANGES OR FILE MODIFICATIONS
    - Check processes for network traffic
      - lsof -i tcp
      - lsof -i udp
      - lsof -c <process/service>
    - Take screenshots and hash malicious files

  - Step 5: Install Threat Hunting Tools:
    - Tripwire is a good example
      - sudo apt install tripwire
        - tripwire -m i (initialize database) **use first
        - tripwire -m c (execute the check)
        - tripwire -m u
        - Add u and c to crontab separately
        - tripwire -m c -I (interactive check)
    - Net-tools also helpful
      - sudo apt install net-tools

  - Step 6: SSH into your servers and repeat...
    - RUN IT BACK (Whoooo Yaaaaaa!!!!!)
    - To ssh into the server... (ssh <user>@<ip_addr>)

Additional Sources/things to think about:
https://github.com/RedefiningReality/Linux-Defence-Materials/tree/main